## Slide 1: UI Architecture Issues
Matt Hollingsworth
University of Tennessee

## Slide 2: Some Concerns
Need some way to easily pass results from one calibration to another
Global state (DACs, AOH bias..) needs to be known in each calibration
Modifications to global state should be kept up with and passed on to
  Calibrations need it
  DB needs it

## Slide 3: Solution
New Framework Object: CassetteSettings
Keeps up with a table of
  DACS per roc
  Slow Hub Parameters
  Trims per roc
  DCOL states per roc
Each Calibration will be fed one of these objects on either construction or Init() (preferences?)
After Calibration(), the calib objects will return another CassetteSettings from a GetCassetteSettings() method
Similar mechanism for FED (use FedCard instead)

## Slide 4: UI’s Involvement
The UI will be calling each of the calibrations, and keeping up with these Settings objects as it goes
The resulting settings object is kept up with at each step
The final settings are calculated based on a cascade merger
Settings serialized into JSON blob and stored in DB as such

## Slide 5: Cascade
Cal 1
Cal 2
Script

## Slide 6: Other comments
All calls which set DACs will go through this object, so we are sure of the state of the system at anytime
Scripts modify “current” settings objects and then write out the changed DACs
Each transition will be saved as separate entry in DB

## Slide 7: Summary
All calibrations will communicate all results via a small set of classes
  PixelFEDCard
  PLTFedCard[]
  CassetteSettings
These three classes will be passed to all calibrations on startup and returned from the calibration on completion (with changes)

## Slide 8: Porting to SLC5
Basically just need to change basic data types to typedef’ed ones
  64-bit: sizeof(unsigned long)
  (const int)8
  32-bit: sizeof(unsigned long)
  (const int)4
  All Systems: sizeof(UInt_t)
  (const int)4
  Etc.