## Slide 1: User Interface Status
Matt Hollingsworth

## Slide 2: Current Functionality
Performs powerup procedure
  As of a month or so ago; changes? Would be helpful to make up-to-date flow charts about this for a while at least
Runs calibrations
  “Sample”, “Levels”, and “Ultrablack” work properly, all of the others have one problem or another that causes crashes due to seg faults at the end
  Saves reported results to database
    Reported results = Output Files, Changes to slow hub, changes to DACs etc
  Ensures system is in defined state before running calibrations
    Uses cascade merge of previous changes to the cassette, falling all the way back to the powerup settings if no modifications
    Also configures the Pixel FED (Framework feeds the PLT cards also, but they aren’t respected on the C++ side yet… can still run the calibs though)
    Sets up triggers properly

## Slide 3: Recent progress
RunManager now does the calibration running
Fixed UltrablackCalibration & LevelsCalibration seg faults
LevelsCalibration output file location saved in DB
Easier API for reporting to DB
  GetResult().SetDACValue(mFec, mFecChannel…)
  GetResult().SetSlowHubValue(…)
  GetResult().outputFiles[“raw”].push_back(“file1.root”)
  GetResult().SetTrimValue(…)
Whenever those ^ are called during calibration, they’re saved to the DB when the UI runs the calibration

## Slide 4: RunManager
Integrated RunManager (C++ side, interface module)
  Uses XDAQ workloops
  Allows python side to query things like Percent Complete, done/not done, etc, while the calibration runs in a separate thread

## Slide 5: Calibration Flow
UI Requests Calibration Run
Python
Added to UI Queue
Waits for Workloop to say “ready”
New Calibration DB Object created, Configuration Cascaded, Cassette DACs Uploaded
Result is passed to queueCalibration()
Runmanager “Ready” flag polled & status update@1Hz
queueCalibration() -> Initialize()
*Feds Initialized
Runs Calibrate();
getPercentComplete() and getStatus() are now accessible
Once done, RunManager sets “Ready” flag
C++
Thread wakes up getRecentCalibrationResult()->DB

## Slide 6: To-Do
Fix remaining seg faults
Make buttons for other calibrations
Maybe update powerup?
Report results through C++ side so values make it to the DB (not necessary right now, if no results are reported, UI runs just like command line utilities)
Integrate DataRun
  Architecture/DB schema supports it, need to decide what exactly we want
  Idea for initial functionality: Select a calibration set, click Run, configuration calculated, uploaded, run is started, output file is kept up with and tied to calibration set
  ?